Licensed under the TAPR Open Hardware License (www.tapr.org/OHL). A copy of the license is included. See file: LICENSE.TXT

GNU General Public License

This program is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.

This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.

You should have received a copy of the GNU General Public License along with this program. If not, see <http://www.gnu.org/licenses/>. A copy of the license is included See file: GPL.TXT

Innovators:	Liselotte Scheu dba Scheus Rainbow Army email: kappa@dekka.com
17600 S. Pacific HWY #20
Marylhurst, OR 97036-0020 usa
Place of performance:	place of business
Employer status:	self-employed (SB)
Contribution:	commercial, material, motivational support

Benjamin Brink	c/o Scheus Rainbow Army
Origin:	self
Innovator representative:	self
New technology representative:	self

Abstract

This hardware design is for building an indoor television (tv) antenna from commonly available parts. The design reduces material construction costs and reduces overall physical profile while matching signal strength and quality of other indoor tv antenna profiles. This design has multiple features: 1. A wide-band balun is built into the antenna. 2. The antenna may be constructed of common materials, such as 75ohm coaxial cable or equivalent. 3. An omnidirectional antenna design reduces installation hurdles associated with directional antennas. 4. No post-installation adjustments; Assumes a fixed position mount. 5. Self-powered; Does not use an amplifier with external power supply.

Table of Contents

Background
I. Problem
II. Technically complete description of innovation
  II.A. Purpose and description of innovation
  II.B. Identification of component parts or steps, and explanation of mode of operation of innovation (with sketches)
  II.B.1. horizontal loop antenna
  II.B.2. “monopole” vertical antenna (optional)
  II.C. Functional operation
  II.D. Alternate embodiments of the innovation
  II.E. Supportive theory
  II.E.1. Charged particles spiral in collapsing or increasing DC current
  II.E.2. Increasingly high voltages reduces power losses from heat
  II.E.3. Eddy currents increase as AC frequency increases
  II.F. Engineering specifications
  II.F.1 Dimensions and measurements
  II.F.2 Materials
  II.F.3 Manufacturing and assembly
  II.G. Peripheral equipment
  II.H. Maintenance, reliability, safety factors
III. Innovation parameters
  III.A. Novel or unique features
  III.B. Advantages of innovation
  III.C. Development or new conceptual problems
  III.D. Test data and source of error
  III.E. Analysis of capabilities
IV. Potential commercial applications and points of contact
V. Other
  V.A. Additional documentation
  V.B. Degree of technology significance
  V.C. State of development
VI. Patent status
VII. Signatures of innovator(s), witnesses

Background

On March 2, 2015 a strategy was developed to demonstrate understanding and application of some principles of electromagnetism used in developing novel ion engines. The strategy is to design a proof-of-concept prototype tv antenna with novel properties. The goal is to make the tv antenna practical and competitively priced. The functional nature of the design was significant from inception. The balun was incorporated into the antenna on May 19, 2015 as a way to improve signal quality and strength.

I. Problem

The original problem statement: How to demonstrate competency with novel ion engine technology while constrained by a frugal budget? Due to the expensive and expansive nature of high-energy physics experimentation, the problem statement has percolated to:

How to design a tv antenna for tv viewers that incorporates design principles not used in conventional tv antenna design and is competitive with market offerings to fund tooling for further development?

II. Technically complete description of innovation

II.A. Purpose and description of innovation

This apparatus is an indoor tv antenna that is smaller than conventional tv antennas and capable of conveying some tv signals usually requiring conventional attic antennas. Its solid-state, high-Q resonator characteristics allows a significant reduction in physical size. The apparatus can be built using mostly common electric materials. The circuit and design is deceptively simple while being innovative, because the apparatus avoids many issues of electrical engineering complexity used in conventional antenna design.

This apparatus incorporates a unique configuration of a wide-band balun by reducing the balun circuit into the physical form of the antenna; Conventional tv antennas usually require a balun between the antenna and receiver to balance impedance. By eliminating the distinctly separate balun from the signal's path to the receiver, the apparatus is capable of delivering a stronger and higher quality signal using a smaller amount of mass and less components. This apparatus also leverages performance features common to small loop antennas.

II.B. Identification of component parts or steps, and explanation of mode of operation of innovation (with sketches)

II.B.1. horizontal loop antenna

The horizontal loop is the primary visible component of the apparatus. On first look, the loop appears to be a simple loop antenna consisting of a conductive cylinder bent into a circular loop ie a torus. On closer examination, the torus contains a wire oriented coaxially. Specifically, the torus loop consists of a coaxial conductive cylinder surrounding a conductor-wire at the axial center of the cylinder with a nonconductive dielectric between the two conductors. The torus is configured most optimally in a closed-loop with a junction that passes the internal conductive-wire externally. Due to practical limits in construction, the torus may have a break of continuity at the junction of the inner coaxial wire.

II.B.2. monopole vertical antenna (optional)

The monopole appears to be a simple monopole antenna consisting of a conductive cylinder oriented vertically. On closer examination, the cylinder contains a wire oriented coaxially. Specifically, the cylindrical monopole surrounds a conductor-wire at the axial center of the cylinder with a nonconductive dielectric between the two conductors.

II.C. Functional operation

The antenna collects tv broadcast electromagnetic (EM) signals and transfers the signals to a transmission line that is usually connected to a tv receiver.

EM signals are initially broadcast from a television terrestrial transmitter at some distance from the antenna. In the US, tv signals are currently transmitted in UHF and VHF wide band frequency spectrums.

A tv signal consists of bits of information encoded into a digital EM signal. The EM signal consists of a combination of synchronized, modular, polarity, amplitude, and phase varying wave cycles and binary fractions (half, forth, eighth, sixteenth etc) of cycles. In the US, tv information bits are embedded via comparative phase offsetting and amplitude modulation such as with 8 bit Vestigial Sideband Modulation (8VSB) or 16 bit Quadrature Amplitude Modulation (16QAM).

An antenna may be simultaneously receiving tv EM signals from multiple transmitters at different angles and azimuths and with different synchronizations. Each distinct change in the accumulated signal represents a possible demarcation of an EM bit (or signal error).
The EM signal operates at a higher bit resolution than the tv signal bit rate. For the entire tv EM signal spectrum, there exists one maximum EM bit resolution (think common denominator frequency) that is approximately equal to a binary fraction (0.5^n) of the tv signal bit rate. An EM bit's frequency is the shortest duration it takes to uniquely identify all EM bits. An EM bit's wavelength is the distance an EM signal travels for the shortest duration of one EM bit.

The EM signal induces a charge in the antenna loop.

The antenna loop's charge most significantly equalizes with ground via current.

Next in significance, the loop induces a current in the opposite direction in the axially oriented wire. The gain is approximately the ratio of the inner circumference of the antenna loop over the circumference of the inner wire.

If the antenna loop is broken at the inner wire junction, the wire's EM signal may be observed to have less current due to a decrease in current from an open-loop configuration.

The axially oriented wire is a closed-loop that connects to the signal path of a transmission line usually in the form the inner wire of a 75ohm coaxial cable, thereby reaching a tv receiver for decoding.

II.D. Alternate emobidments of the innovation

II.E.Supportive theory

The antenna design initially required an external wide-band balun. The balun design published by Chris Trask ( N7ZWY of Sonoran Radio Research, Tempe AZ) entitled “A Single-Core 4:1 Current Balun of Improved Performance” (retrieved from home.earthlink.net/~christrask/Trask4to1Balun.pdf ) seemed particularly appropriate with its wide-band application and elegantly simple design. The balun was incorporated into the antenna when it became apparent that the function of each balun transformer could be substituted with a coaxial conducting tube and wire arrangement.

II.F. Engineering specifications

The EM bit wavelength is small, and its complementary frequency is high. This apparatus requires careful construction --like any device that works in high frequencies. Performance may be affected by variances in dimensions, alignment, noisy connections etc.

complexity in impedance matching

In general, as the length of transmission line increases (over 10% of EM bit wavelength), impedance matching increases in complexity. to existing complexity surrounding impedance matching of a wide-band antenna.

Refer to Figures 1 to 3 for visual representation of definitions.

II.F.1 Dimensions and measurements

For a given signal bit rate or frequency, the loop's perimeter and cylinder's circumference are a fraction of the EM bit wavelength.

Ideally, each circular conductive path, including the coaxial wire loop and wire circumference, resonates at a binary fraction of an EM bit wavelength to increase signal integrity with varying synchronizations of EM signals.

For a given signal bit rate or frequency, the monopole's and cylinder's circumference is either: 1. a fraction of the wavelength, where the fraction is one half to the power of a natural number; or 2. a harmony of multiple Q-resonances for multiple frequency bands or channels, such as television UHF/VHF bands or VHF band reception.

r2 is larger than r1
r2 is circa an integer multiple of r1
A4 x k ≥ A1
c3 = c1 x j1, where j1 is within the range of a positive integer ∓ r4 and c3 > 1
c1, c2, and c3 are circa integer multiples of the length of c4
c5 is an integer multiple of c4

II.F.2 Materials

Testing shows that 75ohm coaxial cable can be awkwardly arranged to fit the minimum performance requirements of the antenna loop and optional monopole.

II.F.3 Manufacturing and assembly

Main ring is connected to secondary rings in a way that minimizes resistance and corona discharge.

Secondary rings' projected planes are oriented at near right angle to main ring's projected plane.

Secondary rings may be equally spaced along the main ring, or grouped and the groupings spaced equally along the main ring.

II.G. Peripheral equipment

Depending on application, a signal generator may be required to connect to an inductor conductor for energy input; Or, an electromagnet positioned at p2 with the magnetic pole oriented along the z axis of symmetry.

II.H. Maintenance, reliability, safety factors

Safety precautions should be used consistent with working with RF, microwave and other high-frequency high-voltage electromagnetic transmitters and where high-energy synchrotron radiation may be present.

Early experiments suggest the apparatus material is susceptible to material degrading at the surfaces. Long-term performance reliability of an apparatus may depend on identifying new materials with properties resistant to degrading; or manufacturing apparatuses with predictable failure patterns.

III. Innovation parameters

III.A. Novel or unique features

Resonance is driven by natural electromagnetic field collapse inducing a complementary field. Whereas the circuit is contained in a passive conductive material instead of an actively generated magnetic field.

III.B. Advantages of innovation

An ion drive may require less energy for same amount of thrust.

Airliners may be able to fly regardless of the presence of volcanic ash.

High voltage power transmission lines may have less losses or power conversion stations built less expensively.

Ultra high frequency motors or centrifuges might operate with greater efficiency.

Levitation may become a practical mode of transport in some situations.

Fluorescent lighting starters may not need to include hazardous and expensive materials such as mercury.

III.C. Development or new conceptual problems

By understanding boundary charge flow, faster and more effective electrical components may be designed with predictable EMI and subsequently less EMI issues.

III.D. Test data and source of error

An apparatus was built with values k=94, k2=1.7, r1= 2.38mm, r2=22.2mm, r3=3.3mm, r4=0.322mm with an induction rod radius of 2.38mm. Apparatus material consisted of low oxygen copper. A flash at a malformed secondary ring was captured via a DSLR using a 3 second f/2.5 exposure, consistent with corona discharge of Nitrogen in air. See file: PRIOR-ART-PROOF-OF-CONCEPT.odt for details.

III.E. Analysis of capabilities

An untuned apparatus appears to work under poor conditions, suggesting this apparatus has potential in achieving design goals.

IV. Potential commercial applications and points of contact

Contact innovator.

V. Other

V.A. Additional documentation: none.
V.B. Degree of technology significance: Major Breakthrough
V.C. State of development: early design and prototyping

VI. Patent status

Released under the TAPR Open Hardware License version 1.0

See file: PRIOR-ART-PROOF-OF-CONCEPT.odt for prior art details.

VII. Signatures of innovator(s), witnesses

Benjamin Brink	20 May 2013
innovator

Liselotte Scheu	20 May 2013
witness

Eric Scheu	20 May 2013
witness